## Slide 1: Python IOT
GPIO, Timers, Management of Battery, Memory & Power

## Slide 2: Python IOT
GPIO Module
Let’s create a module to simplify some of the common activities for our Input & Output devices (LEDs & Buttons)
Let’s start with a Button class
Creating event listeners for buttons can be complex and resource intensive
As we will discuss later in this lesson, resources on a microcontroller are scarce and care should be taken to minimize waste
We will avoid using listeners for buttons

## Slide 3: Python IOT
GPIO Module
Complete Python IOT example 1
https://github.com/jgrissom/Python-IOT/blob/master/lesson02/index.md

## Slide 4: Python IOT
GPIO Module
Now we will add the LED class
Complete Python IOT example 2
https://github.com/jgrissom/Python-IOT/blob/master/lesson02/index.md

## Slide 5: Python IOT
Timers
Before we go further with the Led class, we need to learn about Timers
MicroPython has the ability to use hardware and software timers
Hardware timers are extremely precise and are typically used for applications that utilize servos (think 3-D printers) where precise timing is critical
For what we want, software timers will be perfectly adequate

## Slide 6: Python IOT
Timers
Now that we have determined that we will use software timers, we need to understand that timers are initialized with an operating mode
There are 2 different operating modes: ONE_SHOT and PERIODIC
Timers initialized with the ONE_SHOT operating mode will execute a callback once after a specified period of time
Timers initialized with the PERIODIC operating mode will execute a callback after a specified period of time and continue to execute that callback periodically
https://docs.micropython.org/en/latest/library/machine.Timer.html?highlight=timer#machine.Timer

## Slide 7: Python IOT
Timers
Let’s create some Timer examples
Complete Python IOT examples 3-5
https://github.com/jgrissom/Python-IOT/blob/master/lesson02/index.md

## Slide 8: Python IOT
GPIO Class
Now that we understand how timers work, we can add functionality to our Led class
Let’s add a ONE_SHOT timer to flicker a led
Let’s add a PERIODIC timer to blink a led
Complete Python IOT examples 6-7
https://github.com/jgrissom/Python-IOT/blob/master/lesson02/index.md

## Slide 9: Python IOT
DotStar RGB Led
The TinyPICO comes with a single on-board 2mm RBG Led
DotStar RGB Leds are chainable and individually addressable led lights that we can use to generate colors combining red, green and blue light
Use the RGB Color Slider tool as a reference:
http://www.cknuckles.com/rgbsliders.html

## Slide 10: Python IOT
DotStar RGB Led
We will use some helper modules to simplify accessing the RGB led
Download tinypico.py, micropython_dotstar.py and example.py and save them to your microcontroller
https://github.com/tinypico/tinypico-micropython/tree/master/tinypico-helper
Update your main module to import the example module and reboot the microcontroller

## Slide 11: Python IOT
DotStar RGB Led
Let’s create our own example using the DotStar
We will add a new class to our GPIO module
Complete Python IOT examples 8-10
https://github.com/jgrissom/Python-IOT/blob/master/lesson02/index.md

## Slide 12: Python IOT
Battery Management
Without an external battery gauge, we can only perform simple battery management
A 3.7V lipo battery will discharge quickly from @ 3.9V to 3.7V
It will stabilize between 3.7V and 3.5V for a long time
After that, it will discharge quickly to its critical state @ 3.0V
https://savjee.be/2021/04/max17043-battery-monitoring-done-right-arduino-esp32/

## Slide 13: Python IOT
Battery Management
Since we do not have an external battery gauge, we will create a simple battery management module
Complete Python IOT examples 11-12
https://github.com/jgrissom/Python-IOT/blob/master/lesson02/index.md

## Slide 14: Python IOT
Memory Management
Resources available on a microcontroller like the TinyPICO are limited
RAM is particularly scarce – any variable stored in memory is using up a limited resource
Anytime you use memory to store data, you should be certain to free up that memory allocation as soon as possible

## Slide 15: Python IOT
Memory Management
Let’s examine how memory is managed with Python
Python and many other modern programming languages use reference counting and garbage collection to manage memory

## Slide 16: Python IOT
Memory Management
Before we discuss reference counting, we need to know the difference between primitive and non-primitive (reference) data types in Python
Primitive data types include Integer, Float, Boolean and String
Variables that store primitive data store the data directly in memory
Non-primitive data types include Arrays, Lists, Tuples, Dictionary, Sets and Files
Variables that store non-primitive data store a reference to the memory location where the data is stored

## Slide 17: Python IOT
Memory Management
Let’s examine how primitive/non-primitive data is stored in memory
Complete Python IOT example 13
https://github.com/jgrissom/Python-IOT/blob/master/lesson02/index.md

## Slide 18: Python IOT
Memory Management
Now we can talk about reference counting and garbage collection
When a variable is declared it has a reference count of 1 and memory is reserved for that variable
When another variable points to that value, the reference count increases by 1
When any pointer is deleted, the reference count decreases by 1
When the reference count goes to 0, the garbage collector “frees” the memory allocated to that variable and makes it available to store other data

## Slide 19: Python IOT
Memory Management
Let’s examine how memory is allocated and deallocated for non-primitive data and how we can optimize garbage collection to free memory on demand
We will use the gc class to help us out – there are 3 methods we will use:
  mem_alloc() – returns the number of bytes allocated
  mem_free() – returns the number of bytes free
  collect() – performs garbage collection on demand
Complete Python IOT example 14
https://github.com/jgrissom/Python-IOT/blob/master/lesson02/index.md

## Slide 20: Python IOT
Power Management
Since we have a power button, that is what we are going to use for power management in our application, however, you should be aware of the sleep options available
When you put your ESP32 microcontroller to sleep, you need to configure wake up source(s)
The sources can be a timer or an RTC pin (refer to TinyPICO pinout guide)
For us, that would mean pin 32 – the Yellow Button

## Slide 21: Python IOT
Power Management
Let’s examine how the ESP32 microcontroller can be put to sleep and woken up
Complete Python IOT example 15
https://github.com/jgrissom/Python-IOT/blob/master/lesson02/index.md
For more info, check out the MicroPython documentation on sleep
https://docs.micropython.org/en/latest/library/machine.html?highlight=sleep#machine.sleep

## Slide 22: Python IOT
Morse Code
Revise the Morse Code application created in the previous lesson as follows:
  Use the dotstar rgb led instead of the red led
  Save the dots and dashes to a list
  When the blue button is pressed, try to convert the dots and dashes to the corresponding character and display it – then clear the list