## Slide 1: Python IOT
Synchronous & Asynchronous I/O, Management of Battery, Memory & Power

## Slide 2: Python IOT
Output Module
Let’s create a module to simplify some of the common activities for our Output devices (LEDs & Buzzers)
Complete Python IOT example 1-2
https://github.com/jgrissom/Python-IOT/blob/master/lesson02/index.md

## Slide 3: Python IOT
Output Module
Let’s add a flicker method to our Output class
The flicker method will turn the Led/Buzzer on, wait for a specified delay, then turn the Led/Buzzer off
Complete Python IOT example 3
https://github.com/jgrissom/Python-IOT/blob/master/lesson02/index.md

## Slide 4: Python IOT
Synchronous I/O
The example illustrated the problem with synchronous programming
The sleep method is a blocking method – it blocks code execution until the sleep period has completed
As we add more I/O components, synchronous code is not desirable
If we want to perform multiple tasks simultaneously (like flicker 2 different leds) we need to learn how to create asynchronous code

## Slide 5: Python IOT
Asynchronous I/O
Python has a few different libraries that enable us to handle concurrency or multi-processing
The one we will focus on is asyncio (uasyncio for MicroPython)
Asynchronous programming is a bit challenging, but for what we need to do – it is an ideal solution

## Slide 6: Python IOT
Asynchronous I/O
First, let’s try to understand what asyncio is
https://realpython.com/async-io-python/#async-io-explained

## Slide 7: Python IOT
Asynchronous I/O
With asyncio, we create coroutines using the async/await syntax
“A coroutine is a function that can suspend its execution before reaching return, and it can indirectly pass control to another coroutine for some time.”
https://realpython.com/async-io-python/#the-asyncio-package-and-asyncawait

## Slide 8: Python IOT
Asynchronous I/O
Let’s rewrite the flicker method to use asyncio for a better understanding
Complete Python IOT example 4
https://github.com/jgrissom/Python-IOT/blob/master/lesson02/index.md

## Slide 9: Python IOT
Asynchronous I/O
Let’s add a blink method to the Output class using asyncio
The blink method can be run indefinitely or for a specified number of iterations
Complete Python IOT example 5
https://github.com/jgrissom/Python-IOT/blob/master/lesson02/index.md

## Slide 10: Python IOT
Asynchronous I/O
Detecting a button “press” event is tricky due to switch “bouncing”
When you press a button, 2 pieces of metal come into and go out of contact several times before a solid connection is made
Without switch de-bouncing, a button will detect a press event every time the 2 pieces of metal connect
Generally speaking, this is undesirable

## Slide 11: Python IOT
Asynchronous I/O
Switch de-bouncing can be achieved with a hardware or software solution
The software approach involves using a timer
Instead of creating our own switch debouncing code, we will find a suitable library to handle button events
We will use mpy-lib written by Kevin Köck
https://github.com/tve/mpy-lib/blob/master/button/aswitch.py

## Slide 12: Python IOT
Asynchronous I/O
Create a simple asynchronous push button module
Complete Python IOT example 6
https://github.com/jgrissom/Python-IOT/blob/master/lesson02/index.md

## Slide 13: Python IOT
Asynchronous I/O
If you only need to detect close/open (press/release) events, the async_switch module is what you should use
If you need additional event listeners, like long press, or double-click, there is a more sophisticated version of this library
https://github.com/tve/mpy-lib/blob/master/button/abutton.py

## Slide 14: Python IOT
Asynchronous I/O
Create an advanced asynchronous push button module
This module allows you to create listeners for press, release, long(press) and double(click) events
The default time for long(press) is 1 second
The default timeout for double(click) is 400 milliseconds
Complete Python IOT example 7
https://github.com/jgrissom/Python-IOT/blob/master/lesson02/index.md

## Slide 15: Python IOT
DotStar RGB Led
The TinyPICO comes with a single on-board 2mm RBG Led
DotStar RGB Leds are chainable and individually addressable led lights that we can use to generate colors combining red, green and blue light
Use the RGB Color Slider tool as a reference:
http://www.cknuckles.com/rgbsliders.html

## Slide 16: Python IOT
DotStar RGB Led
We will use some helper modules to simplify accessing the RGB led
Download tinypico.py, micropython_dotstar.py and example.py and save them to your microcontroller
https://github.com/tinypico/tinypico-micropython/tree/master/tinypico-helper
Update your main module to import the example module and reboot the microcontroller

## Slide 17: Python IOT
DotStar RGB Led
Let’s create our own example using the DotStar
Complete Python IOT examples 8-10
https://github.com/jgrissom/Python-IOT/blob/master/lesson02/index.md

## Slide 18: Python IOT
Battery Management
Without an external battery gauge, we can only perform simple battery management
A 3.7V lipo battery will discharge quickly from @ 3.9V to 3.7V
It will stabilize between 3.7V and 3.5V for a long time
After that, it will discharge quickly to its critical state @ 3.0V
https://savjee.be/2021/04/max17043-battery-monitoring-done-right-arduino-esp32/

## Slide 19: Python IOT
Battery Management
Since we do not have an external battery gauge, we will create a simple battery management module
Complete Python IOT examples 11-12
https://github.com/jgrissom/Python-IOT/blob/master/lesson02/index.md

## Slide 20: Python IOT
Memory Management
Resources available on a microcontroller like the TinyPICO are limited
RAM is particularly scarce – any variable stored in memory is using up a limited resource
Anytime you use memory to store data, you should be certain to free up that memory allocation as soon as possible

## Slide 21: Python IOT
Memory Management
Let’s examine how memory is managed with Python
Python and many other modern programming languages use reference counting and garbage collection to manage memory

## Slide 22: Python IOT
Memory Management
Before we discuss reference counting, we need to know the difference between primitive and non-primitive (reference) data types in Python
Primitive data types include Integer, Float, Boolean and String
Variables that store primitive data store the data directly in memory
Non-primitive data types include Arrays, Lists, Tuples, Dictionary, Sets and Files
Variables that store non-primitive data store a reference to the memory location where the data is stored

## Slide 23: Python IOT
Memory Management
Let’s examine how primitive/non-primitive data is stored in memory
Complete Python IOT example 13
https://github.com/jgrissom/Python-IOT/blob/master/lesson02/index.md

## Slide 24: Python IOT
Memory Management
Now we can talk about reference counting and garbage collection
When a variable is declared it has a reference count of 1 and memory is reserved for that variable
When another variable points to that value, the reference count increases by 1
When any pointer is deleted, the reference count decreases by 1
When the reference count goes to 0, the garbage collector “frees” the memory allocated to that variable and makes it available to store other data

## Slide 25: Python IOT
Memory Management
Let’s examine how memory is allocated and deallocated for non-primitive data and how we can optimize garbage collection to free memory on demand
We will use the gc class to help us out – there are 3 methods we will use:
  mem_alloc() – returns the number of bytes allocated
  mem_free() – returns the number of bytes free
  collect() – performs garbage collection on demand
Complete Python IOT example 14
https://github.com/jgrissom/Python-IOT/blob/master/lesson02/index.md

## Slide 26: Python IOT
Power Management
Since we have a power button, that is what we are going to use for power management in our application, however, you should be aware of the sleep options available
When you put your ESP32 microcontroller to sleep, you need to configure wake up source(s)
The sources can be a timer or an RTC pin (refer to TinyPICO pinout guide)
We will attach a new button to pin 33

## Slide 27: Python IOT
Power Management
Let’s examine how the ESP32 microcontroller can be put to sleep and woken up
Complete Python IOT example 15
https://github.com/jgrissom/Python-IOT/blob/master/lesson02/index.md
For more info, check out the MicroPython documentation on sleep
https://docs.micropython.org/en/latest/library/machine.html?highlight=sleep#machine.sleep

## Slide 28: Python IOT
Morse Code
Revise the Morse Code application created in the previous lesson as follows:
  Use the dotstar rgb led instead of the red led
  Save the dots and dashes to a list
  When the blue button is pressed, try to convert the dots and dashes to the corresponding character and display it – then clear the list