## Slide 1: Python IOT
Wi-Fi, JSON, Requests

## Slide 2: Python IOT
Wi-Fi Connection
There are 2 different ways to utilize Wi-Fi on the ESP32:
  One for the station – when ESP32 connects to a router
  One for the access point – so other devices can connect to ESP32
We are going to utilize the station interface to connect the microcontroller to the existing network
Examine the documentation for MicroPython network module
https://docs.micropython.org/en/latest/esp8266/tutorial/network_basics.html

## Slide 3: Python IOT
Wi-Fi Connection
Let’s connect our microcontroller to the Wi-Fi network
Complete Python IOT example 1-2
https://github.com/jgrissom/Python-IOT/blob/master/lesson03/index.md

## Slide 4: Python IOT
JSON
JavaScript Object Notation (JSON) - an open standard file format and data interchange format that uses human-readable text to store and transmit data objects consisting of attribute–value pairs and arrays
https://en.wikipedia.org/wiki/JSON
JSON is used to pass data between server and client using http
Data can be exposed to applications via an Application programming interface (API)

## Slide 5: Python IOT
JSON
MicroPython has a module to simplify working with json data
The json.dump(obj, stream) method convert a dictionary object to a (file) stream and the json.dumps(obj) method converts a dictionary object to a string
The json.load(stream) method converts a (file) stream to a dictionary object and the json.loads(str) method converts a string to a dictionary object

## Slide 6: Python IOT
JSON
Let’s try an example of writing a dictionary object to a json file and reading that file into a dictionary object
Complete Python IOT example 3
https://github.com/jgrissom/Python-IOT/blob/master/lesson03/index.md

## Slide 7: Python IOT
API
Data can be exposed to applications that can communicate using http with an Application programming interface (API)
If the API allows it, we can perform full CRUD operations on data using http requests

## Slide 8: Python IOT
RESTful Web Services
Representational State Transfer (REST) - a software architectural style that defines a set of constraints to be used for creating web services. Web services that conform to the REST architectural style, termed RESTful web services, provide interoperability between computer systems on the Internet.
Wikipedia contributors. (2018, November 24). Representational state transfer. In Wikipedia, The Free Encyclopedia. Retrieved 16:00, November 27, 2018, from https://en.wikipedia.org/w/index.php?title=Representational_state_transfer&oldid=870376984

## Slide 9: Python IOT
RESTful Web Services
The core premise of a RESTful web service is to utilize HTTP request methods (Verbs) to specify an operation for the server to perform
You are probably already familiar with HTTP GET and POST
We need to learn some additional request methods, and under which circumstances each method should be used
In addition, we need to learn how the URL should be formatted to for each operation

## Slide 10: Python IOT
RESTful Web Services
HTTP GET is used to retrieve a specific member of a collection or to retrieve the entire collection (depends on how the request is formatted)
To retrieve the entire collection: https://nugatory.azurewebsites.net/api/word
To retrieve a specific member: https://nugatory.azurewebsites.net/api/word/2

## Slide 11: Python IOT
RESTful Web Services
HTTP POST is used to create a new entry in the collection
https://nugatory.azurewebsites.net/api/word
The request will contain values required to create the new entry

## Slide 12: Python IOT
RESTful Web Services
HTTP PUT is used to replace an existing member of a collection
The request will contain values required to change the new entry

## Slide 13: Python IOT
RESTful Web Services
HTTP DELETE is used to delete an existing member of a collection
https://nugatory.azurewebsites.net/api/word/2

## Slide 14: Python IOT
RESTful Web Services
Examine the nugatory website:
https://nugatory.azurewebsites.net
Examine the nugatory API documentation:
https://nugatory.azurewebsites.net/swagger/index.html
Note: this API does not demonstrate HTTP:PUT

## Slide 15: Python IOT
Requests
We are going to use the urequest module to perform http requests:
https://requests.kennethreitz.org/en/master/
In order to use urequests, we need to install it
Complete Python IOT example 4-6
https://github.com/jgrissom/Python-IOT/blob/master/lesson03/index.md

## Slide 16: Python IOT
Pymon
Remember the game Simon?
If not, you can watch this video:
https://www.youtube.com/watch?v=1Yqj76Q4jJ4
Recreate the memory game using the dotstar rgb led and the red, green, blue and yellow buttons – sound effects not required, however, use the buzzer to indicate an error