## Slide 1: Python IOT
Pulse Width Modulation

## Slide 2: Python IOT
Pulse Width Modulation (PWM)
PWM is a way to get an artificial analog output on a digital pin.
It achieves this by rapidly toggling the pin from low to high.
There are two parameters associated with this: the frequency of the toggling, and the duty cycle.
https://docs.micropython.org/en/v1.15/esp8266/tutorial/pwm.html

## Slide 3: Python IOT
Pulse Width Modulation (PWM)
The duty cycle is defined to be how long the pin is high compared with the length of a single period (low plus high time).
Maximum duty cycle is when the pin is high all the time, and minimum is when it is low all the time
https://docs.micropython.org/en/v1.15/esp8266/tutorial/pwm.html

## Slide 4: Python IOT
Pulse Width Modulation (PWM)
Let’s experiment with PWM
Complete Python IOT example 1
https://github.com/jgrissom/Python-IOT/blob/master/lesson04/index.md

## Slide 5: Python IOT
Pulse Width Modulation (PWM)
In the next series of examples, we will use PWM to change the volume and tone of our buzzer
By adjusting the duty, we can affect the volume and by adjusting the frequency, we can affect the tone
Examine the Note frequency chart on the next slide

## Slide 6: Python IOT
 | Octave 0 | Octave 1 | Octave 2 | Octave 3 | Octave 4 | Octave 5 | Octave 6 | Octave 7 | Octave 8
C | 16 | 33 | 65 | 131 | 262 | 523 | 1047 | 2093 | 4186
C# | 17 | 35 | 69 | 139 | 277 | 554 | 1109 | 2217 | 4435
D | 18 | 37 | 73 | 147 | 294 | 587 | 1175 | 2349 | 4699
D# | 19 | 39 | 78 | 156 | 311 | 622 | 1245 | 2489 | 4978
E | 21 | 41 | 82 | 165 | 330 | 659 | 1319 | 2637 | 5274
F | 22 | 44 | 87 | 175 | 349 | 698 | 1397 | 2794 | 5588
F# | 23 | 46 | 93 | 185 | 370 | 740 | 1480 | 2960 | 5920
G | 25 | 49 | 98 | 196 | 392 | 784 | 1568 | 3136 | 6272
G# | 26 | 52 | 104 | 208 | 415 | 831 | 1661 | 3322 | 6645
A | 28 | 55 | 110 | 220 | 440 | 880 | 1760 | 3520 | 7040
A# | 29 | 58 | 117 | 233 | 466 | 932 | 1865 | 3729 | 7459
B | 31 | 62 | 123 | 247 | 494 | 988 | 1976 | 3951 | 7902

## Slide 7: Python IOT
Pulse Width Modulation (PWM)
Let’s experiment with PWM to control the tone and volume of the buzzer
Complete Python IOT example 2-3
https://github.com/jgrissom/Python-IOT/blob/master/lesson04/index.md

## Slide 8: Python IOT
Pymon
Remember the game Simon?
If not, you can watch this video:
https://www.youtube.com/watch?v=1Yqj76Q4jJ4
Recreate the memory game using the dotstar rgb led and the red, green, blue and yellow buttons – sound effects not required, however, use the buzzer to indicate an error