## Slide 1: Python IOT
Pulse Width Modulation, RTTTL

## Slide 2: Python IOT
Pulse Width Modulation (PWM)
PWM is a way to get an artificial analog output on a digital pin.
It achieves this by rapidly toggling the pin from low to high.
There are two parameters associated with this: the frequency of the toggling, and the duty cycle.
https://docs.micropython.org/en/v1.15/esp8266/tutorial/pwm.html

## Slide 3: Python IOT
Pulse Width Modulation (PWM)
The duty cycle is defined to be how long the pin is high compared with the length of a single period (low plus high time).
Maximum duty cycle is when the pin is high all the time, and minimum is when it is low all the time
https://docs.micropython.org/en/v1.15/esp8266/tutorial/pwm.html

## Slide 4: Python IOT
Pulse Width Modulation (PWM)
Let’s experiment with PWM
Complete Python IOT example 1
https://github.com/jgrissom/Python-IOT/blob/master/lesson04/index.md

## Slide 5: Python IOT
Pulse Width Modulation (PWM)
In the next series of examples, we will use PWM to change the volume and tone of our buzzer
By adjusting the duty, we can affect the volume and by adjusting the frequency, we can affect the tone

## Slide 6: Python IOT
Pulse Width Modulation (PWM)
Let’s experiment with PWM to control the tone and volume of the buzzer
Complete Python IOT example 2-4
https://github.com/jgrissom/Python-IOT/blob/master/lesson04/index.md

## Slide 7: Python IOT
Ring Tone Text Transfer Language (RTTTL)
The RTTTL format is a string divided into three sections: name, default value, and data
Sections are separated by colons
The name section contains the name of the ringtone
https://en.wikipedia.org/wiki/Ring_Tone_Text_Transfer_Language

## Slide 8: Python IOT
Ring Tone Text Transfer Language (RTTTL)
The default value section is a set of values separated by commas, where each value contains a key and a value separated by an = character, which describes certain defaults which should be adhered to during the execution of the ringtone. Possible names are
  d - duration
  o - octave
  b - beat, tempo
https://en.wikipedia.org/wiki/Ring_Tone_Text_Transfer_Language

## Slide 9: Python IOT
Ring Tone Text Transfer Language (RTTTL)
The data section consists of a set of character strings separated by commas, where each string contains a duration, pitch, octave and optional dotting (which increases the duration of the note by one half)
https://en.wikipedia.org/wiki/Ring_Tone_Text_Transfer_Language

## Slide 10: Python IOT
Ring Tone Text Transfer Language (RTTTL)
Entertainer:d=4,o=5,b=140:8d,8d#,8e,c6,8e,c6,8e,2c.6,8c6,8d6,8d#6,8e6,8c6,8d6,e6,8b,d6,2c6,p,8d,8d#,8e,c6,8e,c6,8e,2c.6,8p,8a,8g,8f#,8a,8c6,e6,8d6,8c6,8a,2d6
The name of the ringtone is Entertainer

## Slide 11: Python IOT
Ring Tone Text Transfer Language (RTTTL)
Entertainer:d=4,o=5,b=140:8d,8d#,8e,c6,8e,c6,8e,2c.6,8c6,8d6,8d#6,8e6,8c6,8d6,e6,8b,d6,2c6,p,8d,8d#,8e,c6,8e,c6,8e,2c.6,8p,8a,8g,8f#,8a,8c6,e6,8d6,8c6,8a,2d6
The default duration of a note is a quarter note

## Slide 12: Python IOT
Ring Tone Text Transfer Language (RTTTL)
Entertainer:d=4,o=5,b=140:8d,8d#,8e,c6,8e,c6,8e,2c.6,8c6,8d6,8d#6,8e6,8c6,8d6,e6,8b,d6,2c6,p,8d,8d#,8e,c6,8e,c6,8e,2c.6,8p,8a,8g,8f#,8a,8c6,e6,8d6,8c6,8a,2d6
The default octave is the fifth octave

## Slide 13: Python IOT
Ring Tone Text Transfer Language (RTTTL)
Entertainer:d=4,o=5,b=140:8d,8d#,8e,c6,8e,c6,8e,2c.6,8c6,8d6,8d#6,8e6,8c6,8d6,e6,8b,d6,2c6,p,8d,8d#,8e,c6,8e,c6,8e,2c.6,8p,8a,8g,8f#,8a,8c6,e6,8d6,8c6,8a,2d6
The default beats per minute is 140

## Slide 14: Python IOT
Ring Tone Text Transfer Language (RTTTL)
Entertainer:d=4,o=5,b=140:8d,8d#,8e,c6,8e,c6,8e,2c.6,8c6,8d6,8d#6,8e6,8c6,8d6,e6,8b,d6,2c6,p,8d,8d#,8e,c6,8e,c6,8e,2c.6,8p,8a,8g,8f#,8a,8c6,e6,8d6,8c6,8a,2d6
The first note in the data section is an eighth note, d, 5th octave (default)
The 4th note in the data section is a quarter note (default), c, 6th octave

## Slide 15: Python IOT
Ring Tone Text Transfer Language (RTTTL)
Let’s experiment with RTTTL using a Pulse Width Modulated buzzer
Complete Python IOT example 5
https://github.com/jgrissom/Python-IOT/blob/master/lesson04/index.md
This example is adapted from: https://github.com/dhylands/upy-rtttl

## Slide 16: Python IOT
PWMBuzzer - GPIO
Let’s add a PWMBuzzer class to the GPIO module
Complete Python IOT example 6
https://github.com/jgrissom/Python-IOT/blob/master/lesson04/index.md

## Slide 17: Python IOT
Pymon API
Examine the Pymon Leaderboard
https://pymonscore.azurewebsites.net/
Explore the Pymon API:
https://pymonscore.azurewebsites.net/swagger/index.html

## Slide 18: Python IOT
Pymon
You have everything you need to complete the Pymon IOT game
Add sound effects to each led light up and button press events:
https://en.wikipedia.org/wiki/Simon_(game)#Gameplay
One point is awarded for every correct guess – when the game is finished the total score should be Posted to the Pymon API