## Slide 1: Python IOT
Pulse Width Modulation

## Slide 2: Python IOT
Pulse Width Modulation (PWM)
PWM is a way to get an artificial analog output on a digital pin.
It achieves this by rapidly toggling the pin from low to high.
There are two parameters associated with this: the frequency of the toggling, and the duty cycle.
https://docs.micropython.org/en/v1.15/esp8266/tutorial/pwm.html

## Slide 3: Python IOT
Pulse Width Modulation (PWM)
The duty cycle is defined to be how long the pin is high compared with the length of a single period (low plus high time).
Maximum duty cycle is when the pin is high all the time, and minimum is when it is low all the time
https://docs.micropython.org/en/v1.15/esp8266/tutorial/pwm.html

## Slide 4: Python IOT
Pulse Width Modulation (PWM)
Let’s experiment with PWM
Complete Python IOT example xxx
https://github.com/jgrissom/Python-IOT/blob/master/lesson04/index.md

## Slide 5: Python IOT
Pymon
Remember the game Simon?
If not, you can watch this video:
https://www.youtube.com/watch?v=1Yqj76Q4jJ4
Recreate the memory game using the dotstar rgb led and the red, green, blue and yellow buttons – sound effects not required, however, use the buzzer to indicate an error